## Slide 1
Cisco Easy VPN is an IP Security (IPsec) virtual private network (VPN) solution supported by Cisco routers And security appliances. It greatly simplifies VPN deployment for remote offices and mobile workers. Cisco Easy VPN is based on the Cisco Unity Client Framework, which centralizes VPN management across all Cisco VPN devices, thus reducing the management complexity of VPN deployments. There are three components of the
Cisco Easy VPN solution: Easy VPN Client, Easy VPN Remote, and Easy VPN Server.

## Slide 2
The Cisco Easy VPN Client enables mobile workers to create a remote-access VPN connection to a Cisco Easy VPN Server. Cisco Easy VPN Client refers to the Cisco VPN Client, which is also commonly referred to as the Cisco Software VPN Client.

## Slide 3
The Cisco Easy VPN Remote enables Cisco routers and security appliances to establish a site-to-site VPN connection to a Cisco Easy VPN Server without complex remote-side configuration. Cisco Easy VPN Remote is also commonly referred to as a hardware client.

## Slide 4
The Cisco Easy VPN Server accepts connections from Cisco Easy VPN Client and Remote, ensures that those connections have up-to-date policies in place before the connections are established.

## Slide 5
The Cisco Easy VPN solution uses the Mode-Configuration (Mode-Config) mechanism within the Internet Key Exchange (IKE) to push policy (attributes) from the Easy VPN Server to the Easy VPN Client or Remote. Since this policy is pushed to the client or the remote every time a new tunnel is created, it makes it easier to propagate new policy changes. Mode-Config also enables the Client or the Remote to have minimal configuration in order to establish the tunnel.

## Slide 6
The attributes that can be pushed down through Mode-Config include: internal IP address, internal subnet mask,Domain Name Server (DNS) addresses, Windows Internet Name Service (WINS) addresses, backup server list, domain name, client firewall policy, Cisco IOS Software configuration and Split Tunneling